FORMAT.DOC   (1990-03-06)

Format Specification for AASE Data Exchange Files

1. File Organization

1.1 Single file per flight.  If file exceeds disk size, the flight data should
be continued on subsequent disks, repeating the header information, with 
incremented disk count.  The file names in such cases should reflect that they 
are segments of the same flight file.

Note: If the flight data must extend over more than one disk, it will not be a
single file in the PC or MS DOS sense, but the subsequent file names should be
the same with an incremented file extension number.

1.2 The file naming convention will consist of a two character identifier (this
could be initials of the measured quantity, or of the experimenter, the latter
being best when there are duplicate instruments) and then the flight date.  The
extension should have a letter indicating the flight number for that day 
allowing for the possibility of multiple flights in a day.  Finally there 
should be a number indicating the sequence number for that flight's data, to 
allow for multiple disks required for a single flight.  In any event the 
extension should be added to each file; if there is only one flight and one 
disk the extension would be .A1.  Examples:

SS890127.A1.........1st flight on Jan 27, disk no. 1
SS890129.B1.........2nd flight on Jan 29, disk no. 1
SS890205.A1.........1st flight on Feb  5, disk no. 1
SS890205.A2.........1st flight on Feb  5, disk no. 2

NOTE (90-03-06): The file naming convention has been modified in this release
to use the filename extension to specify the platform (ER2, DC8, Bhh).

1.3 Required header info at the beginning of each file in specified format.


2. Header Format

2.1 Header should supply minimum required information in the format and order 
specified in section 2.4.

2.2 Additional information concerning the data may be added at the end of the 
header segment, after the required information.

Note: It has been requested that a note concerning the number of significant 
figures which are reliable (since we are recording scaled integers) be added. 
This note should be contained in the header segment, after the required
information.

2.3 The number of records specified in the header should include any blank lines
up to the beginning of data.

2.4 Required header information should appear in the order outlined below.

Record  1.  Number of records in the header (including any blank lines).
Record  2.  Experimenter name (last name first).
Record  3.  Disk number; total disks for this flight (separated by a blank).
Record  4.  Mission name.
Record  5.  Flight date and date of data reduction.
            Dates entered as: YY MM DD (separated by a blank).
Record  6.  Mission flight number; Lockheed sortie number (integer numbers
            separated by a blank).
Record  7.  Number of variables (Nv).
Record  8.  Data sample interval, delta t, in seconds.
Record  9.  Number of samples per time hack.
Record 10.  Number of samples per line.
Record 11.  Nv scale factors for converting to engineering units (separated
            by blanks).  The scale factor is the number by which one multiplies
            the integers on the disk file to obtain actual engineering units.
            NOTE: If Nv is large then more than 80 characters may be required
            to specify the scale factors.  In this case more than one line may
            be used to specify the scale factors as long as they can be read as
            one record.
Record 12.  Nv missing values for each recorded variable; this should be a 
            number made up of as many 9's as it takes to fill the data field 
            (separated by blanks).  The missing values should be larger than 
            any good data values.  See NOTE for Record 11.
Record 13.  Name var(1); eng units var(1).
Record 13+1 Name var(2); eng units var(2).
Record 13+2 Name var(3); eng units var(3).
                      .
                      .
                      .
Record 13+(Nv-1). Name var(Nv); eng units var(Nv).

Total number of required records in the header = 13+(Nv-1).  Additional
comments may follow the required records.


3. Data Format

3.1 All data recorded as integer; the time hack can be written as integer or 
real, depending on the experimenter's need for specifying the exact time of 
the measurement.

3.2 Time in GMT elapsed time, cumulative across midnight.

3.3 All data or data blocks are time tagged.

3.4 Time gaps have data field filled with 9's (the appropriate missing value).

3.5 Data organization options.

3.5.1 Time hack on each line (record) followed by data values at that time, as
follows: 

time(1) A(1) [ B(1) C(1) ]
time(2) A(2) [ B(2) C(2) ]
time(3) A(3) [ B(3) C(3) ]

3.5.2 Time hack on separate line followed by block of samples whose first 
value pertains to time hack.  If multiple variables in this option, the blocks
are ordered by variable. 

For single variable:

time(1)
A(1) A(2) A(3) A(4)
A(5) A(6) A(7) A(8)
time(9)
A(9)  A(10) A(11) A(12)
A(13) A(14) A(15) A(16)

For multiple variables:

time(1)
A(1) A(2) A(3) A(4)
A(5) A(6) A(7) A(8)
B(1) B(2) B(3) B(4)
B(5) B(6) B(7) B(8)
time(9)
A(9)  A(10) A(11) A(12)
A(13) A(14) A(15) A(16)
B(9)  B(10) B(11) B(12)
B(13) B(14) B(15) B(16)


4. Examples For File Headers

4.1 Two examples of file headers are given below.  The line numbers enclosed by
square brackets are only for comparison with the header specifications given in
section 2.4 and should not be included in the exchange files.  The second 
example shows that comments may be included, if desired, after the required 
information.

Header example 1:

[ 1]  14
[ 2]  Proffitt, Mike
[ 3]  1 1
[ 4]  AASE Cloud 9
[ 5]  89 01 16  89 01 16
[ 6]  16 45
[ 7]  1
[ 8]  1.0
[ 9]  100
[10]  10
[11]  1.0
[12]  999999
[13]  Ozone ppbv
[14]  This data is perfect.
             .
             .
             DATA
             .
             .


Header example 2:

[ 1]  15 lines in the header 
[ 2]  Scott, Stan  NASA Ames Research Center 
[ 3]  1 3  (disk 1 of 3)
[ 4]  AASE Cloud 9
[ 5]  89 01 16  89 01 18  (year month day of flight and data reduction)
[ 6]  16 45 (AASE flt no./Lockheed sortie no.)
[ 7]  3 variables per sample
[ 8]  1.0 sec data sample interval
[ 9]  1 sample per time hack
[10]  1 sample per line  
[11]  0.1 0.1 0.1  (scale factors)
[12]  99999 9999 9999 (missing values)
[13]  Pressure (mb)
[14]  Temperature (K) 
[15]  True Airspeed (m/s) 
             .
             .
             DATA
             .
             .